## Slide 1
Methodology — the experimental pipeline
From a simulated arm to 45,000 evaluation episodes, in four stages
1. Environment
• UR5e + Robotiq 2F-85 gripper
• Isaac Sim 5.0 / Isaac Lab 2.3.0
• Task: reach, grasp, lift to goal
• Observation: joint state +
• object pose (privileged)
• Action: 6 joint targets + gripper
• Episode: 5.0 s = 250 steps
• 4096 parallel environments
2. Safety cost
• Manipulability floor w ≥ 0.06
• Joint-limit margin 0.175 rad
• Collision floor 0.05 m
• Each term ramps smoothly,
• never a binary switch
• Three terms summed → one budget
• Calibrated on a converged run
• Baseline natural cost ≈ 82
3. Algorithm arms
• PPO baseline (λ pinned at 0)
• cPPO at budget d = 25
• cPPO at budget d = 15
• Identical network, hyper-
• parameters and trainer
• Seeds: 1, 3, 4, 52, 54
• 1500 iterations per run
• 3 arms × 5 seeds = 15 policies
4. Evaluation
• Frozen checkpoint, deterministic
• Exploration noise off
• Eval seeds 101, 102, 103
• (disjoint from training)
• 1000 episodes per seed
• 3000 per policy, 15,000 per arm
• 45,000 episodes in total
• Safety counted per episode
Reward and cost are never summed. The reward carries the task; a separate cost channel carries safety.
This is what lets any measured safety difference be attributed to the constraint rather than to a reward the arms weighted differently.

## Slide 2
Methodology — safety cost: three terms, one budget
Three hazards are scored every step, summed, and held against a single stated budget
Manipulability floor
w = √det(JJᵀ) below 0.06
near-singular: arm loses a direction
Joint-limit margin
clearance under 0.175 rad
joint approaching its mechanical stop
Collision keep-out
link below 0.05 m
monitored, inactive in every run
Aggregate cost
c = sum of the three
one λ governs all
Episodic cost
undiscounted sum
over 250 steps
Budget
d = 25
or d = 15
Every term ramps smoothly from 0 to 1 rather than flipping — a binary flag would give the cost critic no gradient to learn from.
The budget is a number an engineer can defend before training starts, and audit against afterwards.
Thresholds were calibrated on a converged unconstrained run and frozen before the first comparison run.

## Slide 3
Methodology — the three arms, and what each one isolates
The comparison is designed so the constraint's effect can be separated from the machinery that implements it
Validity check: a plain PPO arm was also trained — its stored weights are byte-identical to the baseline arm's, so the implementation term is exactly zero, verified rather than assumed.
PPO (baseline)
cost critic present
λ ceiling = 0
the unconstrained reference
cPPO
cost critic free
budget d = 25
constraint active
cPPO tightened
cost critic free
budget d = 15
binds on every seed
activate the budget
tighten the budget
isolates the constraint effect — the claim of this thesis
isolates budget sensitivity — does it scale?
5 seeds per arm (1, 3, 4, 52, 54) → 15 trained policies. Every quantity is reported with its spread across seeds.
This design answers all three gaps found in the literature: no control arm, no dispersion, one budget only.