## Slide 1
Comparative Evaluation of Constrained and Unconstrained Deep Reinforcement Learning for Safe Robotic Grasping on a UR5e Manipulator in Simulation
Presented by,
MD ABDUR RABBI
Roll: 2031023
Supervised by,
Priyo Nath Roy
Assistant Professor
Dept. of Mechatronics Engineering
Khulna University of Engineering & Technology, Khulna
Date of defense: 08 August, 2026

## Slide 2
Introduction:
UR5: A collaborative arm that shares space with people
  6-DOF, 5 kg payload, 850 mm reach
  Max joint velocity 180 deg/s (𝜋 rad/s)
  with ±360° working limit
  Works next to people, not behind a fence
We use Reinforcement Learning (RL) to train robots

## Slide 3
Background:
Let’s not just train a polity based on reward and penalty - start adding constraints
Reward shapes Policy but Constrains add safety with consistency
  A learned policy can't be inspected like a hand-coded controller — its behaviour is only known statistically.
  Safety on this class of arm is already an active industrial requirement, not a hypothetical
  Validated only by trial and error, after the fact
  This thesis tests the alternative: pull safety out of the reward

## Slide 4
Literature Review:
Positioning Against the Closest Work
Property | Khan et al. | Shen et al. | This thesis
Manipulator | Franka Panda | 4-DOF planar | UR5e
Safety expressed as | Constraint | Reward term | Constraint
Safety quantity | Collision cost | Manipulability | Manipulability + joint limit + collision
Algorithm | PPO-Lagrangian | SAC (unconstrained) | PPO-Lagrangian
Control arm | ✗ | ✗ | ✓
Seed dispersion reported | ✗ | ✓ (5 seeds) | ✓ (5 seeds)
Cost Limit (d) | ✗ (d=25 only) | n/a | ✓ (d=25 and d=15)

## Slide 5
Research Gap:
Three gaps in the closest published work and the design response
3 concrete gaps in the literature and our response to each: no control arm -- we add one; no dispersion -- we report five-seed spreads; one budget -- we test two.
Gap | What the literature does | This thesis's response
No control arm | Trains cPPO vs. PPO, reports the raw difference | Control arm with λ pinned to zero — measures the implementation term directly
No dispersion | Mostly use only 1 seed | 5 seeds for training, 3 for evaluation
One budget only | Fixes cost limit (d) = 25 only | Used cost limit d = 25 & 15 effect read against how hard the constraint

## Slide 6
Objectives:
The main objectives of this thesis are,
    Implementing both the constrained and unconstrained agents
    Isolate the constraint as a cost critic with lambda as a Lagrangian multiplier
    Use different seeds both for training and evaluation
Does a stated budget change safety behaviour — and its predictability?

## Slide 7
Methodology:
Environment Setup
Safety Cost
Evaluation
Algorithm Arms

## Slide 8
Methodology:
Environment Setup
Safety Cost
Evaluation
Algorithm Arms
NVIDIA IsaacSim 5.0.0
IsaacLab 2.3.1
rsl_rl
weld environment
4096 parallel robots for training
1500 iterations
UR5e + Robotiq 2F-85 gripper

## Slide 9
Methodology:
Environment Setup
Safety Cost
Evaluation
Algorithm Arms
Manipulability floor
w = √det(JJᵀ) below 0.06
near-singular: arm loses a direction
Joint-limit margin
clearance under 0.175 rad
joint approaching its mechanical stop
Collision keep-out
link below 0.05 m
monitored, inactive in every run
Aggregate cost
c = sum of the three
one λ governs all
Episodic cost
undiscounted sum
over 250 steps
Budget
d = 25
or d = 15

## Slide 10
Methodology:
Environment Setup
Safety Cost
Evaluation
Algorithm Arms
Proximal Policy Optimization (PPO)
PPO (baseline)
Constraint Proximal Policy Optimization (cPPO)
Budget Limit d = 25 & 15

## Slide 11
Methodology:
Environment Setup
Safety Cost
Evaluation
Algorithm Arms
256 parallel robots
1000 episodes per arm, total 45,000 episodes
3 different seeds (101, 102, 103)
Collision keep-out -- 5 cm above table
Joint-limit margin -- 0.175 rad (10°)
Singularity floor w = √det(JJᵀ) -- w < 0.06

## Slide 12
Methodology:
The 3 arms, and what each one isolates
PPO (baseline)
cost critic present
λ ceiling = 0
the unconstrained reference
cPPO
cost critic free
budget d = 25
constraint active
cPPO tightened
cost critic free
budget d = 15
binds on every seed
activate the budget
tighten the budget
isolates the constraint effect — the claim of this thesis
isolates budget sensitivity — does it scale?
5 seeds per arm (1, 3, 4, 52, 54) → 15 trained policies. Every quantity is reported with its spread across seeds.
This design answers all three gaps found in the literature: no control arm, no dispersion, one budget only.

## Slide 13
RESULT:
0.4
0.3
0.2
0.1
0.0
0
500
1000
1500
0.08
0.06
0.04
0.02
0.00
0
500
1000
1500
0.0006
0.0004
0.0002
0.0000
0
500
1000
Training iteration
Training iteration
Training iteration
Cost contribution
(a) Singularity
(b) Joint limit
(c) Collision
PPO (baseline)
cPPO (d = 25)
cPPO (d = 15)
Mean Reward:
  PPO(baseline) :
  cPPO(d=25) :
  cPPO(d=15) :
Lifting-object reward:
133.06
132.18
134.09
9.467
9.437
9.441

## Slide 14
RESULT:
*Tail mean(last 10% of the training data)
The constraint costs nothing measurable
Constraining the policy did not cost task performance at either budget.

## Slide 15
RESULT:
Safety: fewer true singularities, zero joint-limit contact

## Slide 16
Conclusion:
A stated budget changes what a policy does — mostly by making it predictable
    Constraining the policy reduces unsafe behaviour
    At no measurable task cost.
    An unanticipated effect is on consistency
Future Work:
  IBVS systems
  Sim-to-real application
  PID Lagrangian
  More Seeds implementations

## Slide 17
Key Resources:
[1] Altman, E. (1999). Constrained Markov Decision Processes. Chapman & Hall/CRC.
[2] Schulman, J. et al. (2017). Proximal Policy Optimization Algorithms. arXiv:1707.06347.
[3] Achiam, J. et al. (2017). Constrained Policy Optimization. Proc. ICML, PMLR 70.
[4] Ray, A., Achiam, J., & Amodei, D. (2019). Benchmarking Safe Exploration in Deep RL. OpenAI.
[5] Stooke, A., Achiam, J., & Abbeel, P. (2020). Responsive Safety in RL by PID Lagrangian Methods. Proc. ICML, PMLR 119.
[6] Yoshikawa, T. (1985). Manipulability of Robotic Mechanisms. Int. J. Robotics Research, 4(2).
[7] Henderson, P. et al. (2018). Deep Reinforcement Learning That Matters. Proc. AAAI 32(1).
[8] Khan, F. et al. (2026). RL for Precision Grasping and Safety-Critical Coordination in a Robotic Arm. Intelligent Service Robotics, 19(16).
[9] Shen, Y. et al. (2022). RL-Based Reactive Obstacle Avoidance for Redundant Manipulators. Entropy, 24(2).

## Slide 18
Key Resources:
[10] Ferreira, H. C. & Barbosa, R. S. (2025). Deep RL for Adaptive Robotic Grasping in Simulated Dynamic Environments. Future Internet, 17(10).
[11] Shahid, A. A. et al. (2022). Continuous Control Actions Learning and Adaptation for Robotic Manipulation through RL. Autonomous Robots, 46.
[12] Mittal, M. et al. (2023). Orbit: A Unified Simulation Framework for Interactive Robot Learning Environments. IEEE RA-L, 8(6).
[13] Rudin, N. et al. (2022). Learning to Walk in Minutes Using Massively Parallel Deep RL. Proc. CoRL, PMLR
[14] Universal Robots A/S (2023). UR5e Technical Specifications. Product datasheet.
[15] Khan, M. M. (2025). Enhancing Manipulator Control Through IBVS Techniques Using ROS2. BSc thesis, KUET.

## Slide 19
THANK YOU